## Slide 1
PEAS: A Robust Energy-conserving Protocol
for Sensor Networks
Probing Environment
Adaptive Sleeping
Fan Ye, Gary Zhong, Songwu Lu and Lixia Zhang UCLA
Goal
Extends a sensor network’s lifetime many times longer than those of individual sensor nodes
Means
Deploy sensor nodes at densities much higher than needed for normal operation
Keep a subset working while turning off others
Sleeping nodes replace failed or energy-exhausted ones when necessary
Challenges
Nodes are prone to unexpected failures in a harsh or hostile environment
  The protocol has to be robust against such failures
Nodes may have stringent memory, computing resources
  The protocol has to be very light-weight to run on small, simple sensor nodes
  Why it is necessary?
    Probings are needed to find and replace dead working nodes
    Probings consume energy
    Keep the probing rate high enough to replace dead working ones on time, but not to consume too much energy
  How?
    A working node measures the aggregate probing rate
    Piggyback the measured rate in REPLY messages
    Probing nodes adjusts their rates accordingly
Keep the aggregate probing rate of a working node’s probing neighbors at some constant level
  Metrics
    Data delivery lifetime: when success ratio fells below a threshold
    Sensing coverage lifetime: when coverage ratio fells below a certain threshold
    Energy overhead: energy consumed in protocol operations, including PROBE and REPLY messages
  Main results
    Both the data delivery and sensing coverage lifetimes increase linearly in proportion to the number of deployed nodes
    Robust against node failure rates of up to 38%
    Energy overhead is less than 1% of total energy consumption
PROBE
REPLY
PROBE
Node 1 broadcasts a PROBE within a probing range Rp
No working node is within Rp to node 1
Node 1 becomes a working node
1
Probing node 2 broadcasts a PROBE within Rp
Working node 3 sends back a REPLY
Node 2 goes back to sleep again
2
3
Working node 4 fails or exhausts energy, and stops working
4
Probing node 5 broadcasts a PROBE within Rp
The only node within Rp (node 4) is dead, thus no REPLY is sent to node 5
5
Node 5 becomes a working node, replacing dead node 4
Keep a relatively constant density of working nodes
Analytical Results
  When N Nodes are uniformly distributed in [0, l]2, the set of working nodes are connected asymptotically almost surely if
    N Rp2 > 2 l2 lnl
    The transmitting range Rt >= (1+ 5) probing range Rp
  The average length of interruption due to a dead working node is 1/, where  is the aggregate probing rate
  Complexities
    State complexity at each node O(1) since no per-neighbor state is required
    Computing and energy overhead both O(1)
Performance Evaluation
Data delivery lifetime vs. deployed node number
Sensing coverage lifetime vs. deployed node number
Data delivery lifetime vs. node failure rate
Sensing coverage lifetime vs. node failure rate