## Slide 1
A Two-Tier Data Dissemination Model
for Sensor Networks
Query and Data Forwarding
Fan Ye, Haiyun Luo, Jerry Cheng, Songwu Lu and Lixia Zhang UCLA
Approach
Each source builds a virtual grid and stores data at nodes close to grid crossings
A mobile sink floods locally to find a grid node
Queries and data traverse upper grid tier and lower cell tier in reverse directions to reach sources and sinks, respectively
When the sink moves, upper tier forwarding changes incrementally, thus avoiding global floodings
  A source builds a grid
    Given grid size , the source sends data announcement messages using geographical forwarding
    The node closest to a grid crossing becomes a DN (dissemination) node
  A query traverses two tiers to reach the source
    A sink locally floods a request within a cell size to find an immediate dissemination node ( IDN )
    The query goes to the IDN node, then travels along the grid to reach the source
  Data traverse two tiers in reverse order
    Data first travel along the grid to reach the IDN node
    Then go to the sink from the IDN node
A source sends data to a sink
  Metrics
    Data success ratio: the percentage of data reports that successfully reach sinks
    Energy consumption: the amount of energy used in transmitting and receiving messages
    Delay: the average time it takes sinks to receive data reports
  Main results
    Success ratio remains high, energy consumption scales as the number of sinks or sources increases, or sinks’ moving speed increases
    Robust against unexpected sensor node failures
Performance Evaluation
Success ratio vs. sink and source numbers
Energy vs. sink and source numbers
Success ratio vs. sinks’ moving speeds
Energy vs. sinks’ moving speeds
Goal: Deliver data to mobile sinks without interruption, even when these sinks are in continuous motions
Stimulus
Source
Sink
Sink
Sink
source
data
query
sink
source
data
query
sink moves
here
another sink
  If a sink moves
    It locally floods a new request to find a new IDN node
    A query goes to the IDN nodes, then to the direction of the source along the grid
    The query stops at a DN that is already receiving data
  Multiple sinks
    Each sink finds its IDN node
    Each sink sends a query upstream to the source
    Data flow to a sink when its query reaches a DN that is already receiving data
The sink moves and another sink appears
Grid Maintenance
  Upstream information duplication
    Each DN replicates its upstream DN’s location, ID, etc. at its neighbors
    A query is forwarded to the upstream DN by one of the neighbors of a failed DN
    A data report is forwarded to three other downstream directions, and only those need data send back queries to restore forwarding states